## Slide 1
GOVERNMENT OF ROMANIA
Structural Instruments
2007-2013
Sectoral Operational Programme
„Increase of Economic Competitiveness”
“Investments for Your Future”
Extreme Light Infrastructure – Nuclear Physics (ELI-NP)
Quest for laser driven experiments at ELI-NP
EUROPEAN UNION
Project co-financed by the European Regional Development Fund
Daniel Ursescu
19.06.2014, DFT Seminar, IFIN-HH

## Slide 2: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 3: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 4: Extreme Light Infrastructure
2006 – ELI on ESFRI Roadmap
ELI-PP 2007-2010 (FP7)
  ELI-Beamlines (Czech Republic)
  ELI-Attoseconds (Hungary)
  ELI-Nuclear Physics (Romania)
ELI-DC (Delivery Consortium): 2010
Legal entity: April 2013
Czech Republic, Hungary, Romania, Italy, Germany, UK

## Slide 5: ELI-NP Main Equipment
High power laser system, 2 x 10PW maximum power
Thales Optronique SA and SC Thales System Romania
Gamma beam, high intensity, up to 20MeV,
produced by Compton scattering of a laser beam
on a 700 MeV electron beam produced by a warm LINAC
EuroGammaS Association:
Instituto Nazionale di Fisica Nucleare (Italy)
Università degli Studi di Roma ”La Sapienza” (Italy),
Centre National de la Recherche Scientifique (France),
ALSYOM S.A.S. (France), ACP Systems S.A.S.U. (France),
COMEB Srl (Italy) ScandiNova Systems (Sweden), etc.

## Slide 6: ELI–NP Nuclear Physics Research
Nuclear Physics experiments
Photo–fission & Exotic Nuclei
Nuclear Photonics (NRF)
Photo–nuclear reactions and structure
Nuclear Astrophysics
complementary to other ESFRI Large Scale Physics Facilities (FAIR, SPIRAL2)
Laser–Target interaction characteristics: NP diagnostics
Laser Ion driven nuclear physics experiments
Strong fields QED. Towards High field (Laser + Gamma) and Plasma
Applications based on HPLS and High intensity laser and very brilliant g beams complementary to the other ELI pillars
ELI–NP in Romania selected by the most important science committees in Europe – ESFRI and NuPECC, in the ‘Nuclear Physics Long Range Plan in Europe’ as a major facility

## Slide 7
ELI–NP Project Timeline
WB &Feasibility Study
Cost estimate 293M€
Preparation of the Application
---TDR’s----------Cons
2016- 2018
2015-2017
2010 2011 2012 2013 2014 2015
E.C. Eval. & Funding Approval
Procurement Gamma Beam
Procurement Laser System
Experiments Instruments
Gamma Beam – installation
Laser System – installation
Civil engineering construction

## Slide 8
June 14th, 2013

## Slide 9
August 23, 2013
June 14, 2013
October 31, 2013
March 13, 2014
Building progress

## Slide 10: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 11
to compressors
2 x 0.1 PW
2 x 1 PW
2 x 10 PW
Provided by THALES - France
Based on the principle of OPCPA

## Slide 12
2x10PW Laser System
Thales Optronique SAS and S.C. Thales System Romania SRL
July 12th, 2013

## Slide 13: Lay –out of the Laser –Gamma Beam and experimental halls at ELI-NP

## Slide 14: Gamma Beam System
EuroGammaS Association: Instituto Nazionale di Fisica Nucleare (Italy)
and Research Institutions and Companies from
Italy, France,
Sweden, UK,
Germany, Denmark,
Slovenia, Spain
March 19, 2014

## Slide 15: ELI–NP Scientific Coordination
  Gamma Beam Delivery & Diagnostics
  NRF Experiments and applications
  Photo–fission experiments
  (g,n) experiments
  (g,p) experiments
  Applications, including (g,e+)
  Convener local liaison
Scientific Director
Gamma Beams System
High–Power Laser System
  Laser delivery and beam lines
  Laser Driven NP experiments
  Strong field QED
  Laser + Gamma interaction
  Applications
  Convener local liaison
International Workgroups for TDR’s
Engineering bureau : Building Interface&Transversal Technical proposals
Safety RP Dosimetry, Vacuum, Control system
Alignments, Laboratories, Utilities

## Slide 16: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 17: Main working groups
TDR Laser Beams Delivery: convener Gilles Cheriaux (LOA, France)
TDR1: Laser Driven Nuclear Physics – convener Markus Roth (TU Darmstadt, Germany)
TDR2: Strong Field QED – convener Paul McKenna, (SUPA, UK)
TDR3: Combined Laser-Gamma experiments – convener Kensuke Homma (Hiroshima University, Japan)
TDR4: Irradiated Materials Science – convener Marilena Tomut (GSI, Germany)
Vacuum related issues – M Toma, ELI-NP
Alignment related issues – Cristian Petcu, ELI-NP
Radioprotection related issues – Sorin Bercea, ELI-NP
EMP related issues – Marius Gugiu, ELI-NP
Control systems related issues – Mihail Cernaianu, ELI-NP

## Slide 18: ELI–NP Experiment Building
Experiments
8 experimental
areas
HP Lasers
7000 m2
E1 10PW
E2,NRF
E7,2X10PW
E8,Gamma
Nuclear reactions
E5 1PW @ 1 Hz
E4 0.1PW @ 10 Hz
E3 Positron
source
E7,QED High field
gamma + electrons
E6 10PW

## Slide 19
Preliminary , first step lay out of High Power Laser Experiments in
E1,E6,E5,E7
TDR1,TDR2, TDR3,TDR4
First generation of experiments to be implemented
Goals: Precise technical description , Target interaction chamber, Target technologies , vacuum, diagnostics and laboratories

## Slide 20: HPLS Delivery
Mirror
Adaptive optics
Polarization control
Relay imaging
2x10PW
interaction area
Strong field QED
10 PW
Ion–driven NP
10 PW
E6
E1
E7

## Slide 21: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 22
Laser driven Nuclear Physics Experiments TDR1
Convener :M. Roth ELI-NP F. Negoita +WG members
2.1 Nuclear fusion reactions from laser-accelerated fissile ion beams
  2.1.1 RPA for heavy ions
  2.1.2 Stopping power of very dense ion bunches
  2.1.3 Fission-Fusion reaction mechanism
2.2 Nuclear (de)excitation induced by lasers
  26Al case
2.3 Nuclear Astrophysics in Laser plasmas
  2.3.1 13C(4He,n)16O and 7Li(d,n)4He-4He

## Slide 23: The experiments for Laser Driven Nuclear Physics for E1 area at ELI-NP
Nuclear fusion reactions from laser-accelerated fissile ions, to understand the nucleosynthesis of heavy elements. The neutron rich nuclei (with N=126) produced in the laser induced fission and fusion reactions in a Thorium target, will make possible the study the production mechanism of heavy elements (through the r-process) . There is an experimental group to study:
Radiation Pressure Acceleration of heavy ions;
The Stopping Power for Intense Ion Bunches and
The fission – fusion reaction mechanism.
The Bethe –Bloch equation for the stopping power for the ion (eq. 1) has two terms: the binary collision term (T1) and the long range collective interaction term (T2). This allows the study of potential reduction of atomic stopping power or ultra dense ion bunches.
Laser Induced Nuclear (De)excitation, to study the excitation levels and lifetime of 26Al.
Nuclear astrophysics in laser induced plasma, to study the nuclear reactions relevant in nucleosynthesis: 13C (4He, n) 16O ; 7Li (d, n) 4He ;

## Slide 24: Laser Driven NP at ELI–NP
Study of exotic nuclei of
astrophysical interest
produced using high
density ion bunches :
fission–fusion reactions.
n–rich nuclei around N = 126
waiting point
Study of heavy ions acceleration mechanism at laser intensities > 1023 W/cm2
Deceleration of very dense electron and ion beams
Understanding influence of screening effect on stellar reaction rates using laser plasma
Nuclear techniques for characterization of laser–induced radiations
Fission
fragments
Fusion products
Reaction target
232Th: ~ 50mm
CH2 ~ 70 mm
< 1 mm
Production target
CD2: 520 nm
232Th: 560 nm
high-power, high-contrast laser:
300 J, ~30 fs (10 PW)
~.1023 W/cm2
focal diam. ~ 3 mm
D.Habs, P.Thirolf et al., Appl. Phys. B 103, 471 (2011)
key
nuclei
15 neutrons away
from r process path (Z≈ 70))

## Slide 25: The scheme for fission-fusion experiments
232Th, 50 μm thick
CH2 70 μm thick
Fusion products
Fission fragments
The experiment proposed with 8.5 -17 PW laser beam (150-300 J), ultra-short pulses (32 femto-seconds). For a focal diameter of 3 micrometers, the Laser power was 1.2 ·1023 W/cm2.
232Th, 560 nm thick
CD2 520 nm thick
1 mm
Fission:
Beam: H, C, 232Th
Target: C, 232Th
Fusion from two light fission(target-like and beam –like) fragments
Target like fission fragments:
Beam like fission fragments:
D.Habs, P.Thirolf et al., Appl. Phys. B 103, 471 (2011)

## Slide 26: Configurations possible with a 1PW and 10 PW laser beams (left fig) or two 10 PW laser beams.
F/3
F/6
1 PW of up to 250 J of compressed Laser beam
1PW
10 PW
10 PW
10 PW
F/3
F/3
10 PW

## Slide 27: The required equipment in E1 area and the experimental challenges
Challenges: Laser Acceleration of Heavy Species (RPA), the Optimization of target structure and shape, the repetition rate capability, the characterization of stopping range for Laser (with investigation of potential collective effects).
The development of the identification technique of the reaction products. : setup for precision mass measurements, wide acceptance separator for fission products, decay spectroscopy for short lived species.
The novel laser-ion acceleration (RPA) of the new species, allows the generation of ultra-dense ion pulses and the fission-fusion reaction mechanism.
Characterization of reaction products (decay spectroscopy)
Precision mass spectroscopy (Penning Trap or MR-TOF)
The ELI-NP Laser will have 2 X 150 Joules/pulse, 30 femto-seconds /per pulse to get and intensity of I=1023 W/cm2

## Slide 28: Nuclear excitations with Ultra Intense lasers
Recherche
I LP
M.M.Aléonard,
F.Hannachi, F.Gobet, M.Gerbaux, C.Plaisir, M.Tarisien, J.N.Scheurer

## Slide 29
Some orders of magnitude
1- Time scales
Laser wave period for 1 eV (1µm) photons: T = 4.10-15 s = 4 fs
Pulse duration (LOA ) T = 30 fs i.e. 80 % of the energy in 8 periods
Bohr orbital electron period t= 4 10 –17 Z-2 s (Al: 0.02 fs; Ca:0.01fs)
2 - Electric field scales
Intra-nuclear electric field: Fn = 1019 V/cm
Binding electric field in hydrogenoid atom Fe = (Z3 /n2) 2.7 109 V/cm
13Al Fe ~ 6 1012 V/cm 20Ca Fe ~ 2 1013 V/cm
laser wave electric field as a function of the intensity: Fl = 13.7 I 0.5
I(W/cm2) 1014 1020 1022 1024 1026
F1(V/cm) 108 1011 1012 1013 1014

## Slide 30
Electrons, g, protons with
high energy (keV – MeV)
Warm and dense plasma
High electromagnetic fields: 1011 V/cm, 1000 T
Nuclear excitation and reaction yields in plasmas?
Nuclear Excitation by Electronic Capture (NEEC) in plasmas?
Modification
of bound energy
and nucleus – electron
couplings
What kind of nuclear physics with plasma created with high-power lasers?
Free electrons
Bound electrons
Modification
of nuclear deexcitation processes in plasma?
(Internal Conversion)

## Slide 31
Nuclear Reactions in Plasmas
Nuclear Astrophysics
ELI-NP Meeting Darmstadt March 24, 2014
S. Tudisco
Collaboration
-LNS

## Slide 32
Methodology
TNSA - Target Normal Sheath Acceleration 1018 - 1020 W/cm2
Macchi et el. Rev of Mod. Phys, 85 (2013) 751
D.C. Carrol et al., New J. of Phys. 12 (2010) 045020
Peta-Watts
Secondary
1018 Atoms/cm3
Two laser beams generating two colliding plasmas
Secondary Nd:YAG
6×1020 W/cm2
Fixing TNSA regime
(an than the maximum ions energy)
the total ions number is determined by: Laser intensity, focal spot and target thickness

## Slide 33: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 34: Strong Field QED
ELI–NP delivering pulse at > 1023 W/cm2 will enable
this exciting new regime to be investigated

## Slide 35
High Field QED Experiments at ELI–NP
  High Field Physics in Beam-Beam Interactions
  Producing suitable secondary electron beams, gamma beams and controlling the laser pulses
  Nonlinear Compton Scattering
  Classical and Quantum kinetic radiation reaction effects
High Field Physics in Dense Plasma (Solid) Interactions
Intense synchrotron gamma-ray generation
Radiation reaction
Electron-positron pair production

## Slide 36: High Intensity Laser Fields and QED experiments at E6 area

## Slide 37: High Field Physics with Beam-Beam interactions (E6
Laser beam with intensity >1021 W/cm2 produces relativistic electrons in a gas plasma. The electrons are accelerated in the laser field. The work done by the Laser field a0=eA/(mc2). Electrons gain a longitudinal momentum a02. If a laser beam can be scattered off a counter propagating electron beam with ⋎>>1, to produce a gamma beam with shifted frequency by a factor 4·⋎2 . The phenomena that can be studied are:
Classical Radiation Reaction, to understand how charged particles interact with their own radiation field. If a0>>1 significant momentum is taken up by the electron oscillating in Laser Field and the radiation force is large. The Radiation Reaction can be treated as perturbation [1] or with a non-perturbative approach [2].
Nonlinear Compton Scattering is seen in low intensity laser beam 1< a0 < 10 and not-focused laser beam pulses to extend the interaction time and treat the laser as plane waves. Electron bunches (10 MeV) interacting head on with such laser beam, emit radiation with an intensity that depends on the mass shift of the electrons.
Classical and quantum kinetic radiation effects. Radiation Reaction tends to reduce the energy spread of the electrons when 50 MeV electron bunch collides head-on with the laser pulse of a0 =10. Quantum effects become important for 1 GeV electrons collide with a laser with a0=70, such that the Radiation Reaction increases the spread of electrons. Both effects could be studied at ELI-NP.

## Slide 38: High Field Physics with Beam-Beam Interaction
Non-linear optics in relativistic plasma. At high laser intensity the bounce frequency of electrons trapped in trapped ponderomotive force is bigger than plasma forces. Coherent scattering in plasma, can compress laser pulses and enhance the beam intensity, allows the control of the pulse duration, the focusing and the contrast enhancement.
Electron beam generation using Laser Plasma Wake Field Acceleration. In the first stage, at ELI-NP, an electron beam will be accelerated to 5-10 GeV in the 10 PW Laser field focused in a 1 meter long plasma cell (with density 1016 – 1017 cm-3). The electron beam will be suitable for radiation reaction studies.
Betatron gamma rays generation: The LWFA electrons can be used as a source of gamma radiation. Hard X rays emitted from femto-second laser-produced plasma and betatron X rays from LWFA electrons, were reported [1].

## Slide 39: High Intensity Laser Fields and QED experiments at E6 area

## Slide 40: High Field Physics with solid-laser interaction (for E6 area)
Two main QED processes are important in laser-solid interaction: a) Thomson scattering (e-+⋎L ⇾ e- + ⋎R ) in which 40% of electron energy is damped in the Laser field, via synchrotron radiation emission. b) Pair production ⋎L + ⋎R ⇾ e- + e+ . The two processes are important when the parameter η= γ/E (Ep +v x B), is almost unity. Here Ep is the perpendicular component of the electric field. The Lorentz factor γ >300 and η >0.2 and I=1024 W/cm2
Intense synchrotron gamma rays produced from electrons accelerated by Laser’s electric field, when the damping force exceed the Lorentz force on electron. The ELI-NP laser beams with 10PW and 1023 W/cm2 should enable the onset of radiation damping, when >35% of the Laser energy is converted to intense synchrotron radiation.
Electron –Positron pair production : a) an electrons with E>1.022 MeV produces electron-positron pair (the single stage Trident process) and b) electron emits a synchrotron radiation E>1.022 MeV that generates the electron – positron pair (the two stage Bethe Heitler process). A cascade of gamma rays and e-e pairs is predicted at laser intensities >1024 W/cm2.

## Slide 41: Requirements for laser beam control and the characterization (at E6 area)
Highest possible intensity >1023 W/cm2
Shot focal length F3 (or shorter) off-axis parabola mirrors.
Two 10 PW beams combined on target with coherent addition of the pulses, phase front tilt control
Polarization control needed, to switch from circular to linear polarization.
Ultra high intensity 1013:1 contrast is needed for nano-seconds pulses and 1014:1 at pico-seconds pulses.
Temporal shaping and control of rising edge of the laser pulse
Spatial shaping and control of focal spot distribution with adaptive optics.
Debris mitigation using suitable pellicles (with minimum front distortion) to cover the surface of the mirrors. Inter-changable optics required to minimize the downtime.

## Slide 42: Laser diagnostics required for E6 area
Laser dignostics
Intensity temporal contrast measurements;
FROG Frequency Resolved Optical Gating Diagnostics.
Measurement of the laser focal spot energy distribution
The degree of the temporal overlap measurement
Synchronized optical probe to characterize the density gradient at target front surface
Near and far field monitoring of the laser beams
Electron beam diagnostics:
energy spectrometer,
beam profile,
charge (Faraday cup, ICT and calibrated),
emittance measurement,
beam transport system.
Plasma diagnostics for beam-beam experiments:
Thomson scattering
interferometer

## Slide 43: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 44: TDR3 Combined laser - gamma experiments
Dark field search (Four-wave mixing in the vacuum)
QED birefringence studies
Electron induced nuclear processes investigated with gamma beams
Gamma-gamma scattering
Gamma assisted electron-positron pair production in vacuum; requires:
  Nonlinear Thomson scattering or
  X-ray laser / high order harmonics driven Backscattering gamma source
  Bremsstrahlung source driven by laser produced ultrarelativistic electron bunches

## Slide 45
Combined laser-gamma
Experiments standard set-up
Combined laser-gamma
Nonlinear backscattering set-up
Laser-only
Nonlinear backscattering set-up
Experiments at E7
Interaction
point
Focusing mirror
e-/gamma from GBS
Laser pulse
Laser pulse
Plasma mirror
Gas jet
e- from GBS
e- from LWA
ELI-NP Workshop 2013 / K. Homma
Notes: 45
45

## Slide 46
Experiments at E7: Nonlinear Scattering as extension method for the gamma range at ELI-NP
Focal distance correlation with the peak power in focus
The spectrum of the normalized total scattered radiation for a=65.9. (Ij is the intensity of the jth harmonic radiation).
Ionel, Ursescu, LPB2014
How to reach peak power
Harmonics in the gamma spectra to be seen
Notes: 46

## Slide 47
X-ray laser driven gamma source experiments proposal at ELI-NP
Banici,Ursescu et al, Optics Letters 2012:
X-ray laser driven with 200mJ pump energy @13.9 nm and 10Hz
Cojocaru, Ursescu et al, Optics Letters 2014
Available 100Hz laser for ELI-NP gamma facility with at least 200mJ energy/pulse
J. Rocca group, Optics Letters 2012:
Demonstrated 100Hz operation of an XRL driven with 1000mJ pump energy @13.9 nm and 10Hz
On-going Laserlab3 experiment for 200mJ pumped 100Hz X-ray laser @ MBI, Germany (D. Ursescu)
Notes: 47

## Slide 48: Specific technologies
Target manipulation (gas target, solid target for bremsstrahlung generation)
Beam manipulation (plasma mirrors, mirror shifting)
Vacuum pipes
Vacuum pumping
Diagnostics of the beams at experimental areas (LBD?)
Detection and data processing
Beam dumps
Logistics

## Slide 49: Laser-electron interaction
g
g detectors
600MeV e-
e-
e+
D. Habs et al.
D. Habs et al.
arXiv:1010.4528 [hep-ph]
N. Elkina et al.
N. Elkina
ELI-NP Workshop 2013 / K. Homma

## Slide 50: TDR3: Electron induced nuclear processes investigated with gamma beams

## Slide 51: Content
Project outline
Main tools
Laser driven experiments
  TDR1: Laser driven nuclear physics
  TDR2: Strong field QED
  TDR3: combined laser gamma experiments
  TDR4: material science and applications

## Slide 52: TDR4: Applications of Material Science
• testing new materials for fusion and fission energy application
• testing of new materials for accelerator components
• testing materials for space science (electronics components,
hypervelocity impacts)
• surface and volume modification; micro- and nano-technology)
• biological science research (effects on bio-molecules, cells)
• testing radiation hardness and developments of detectors
• irradiated optical components testing
Potential partners: GSI, CERN, GANIL, Politecnico di Torino, ESA,
Fraunhofer-Institut für Kurzzeitdynamik Ernst-Mach-Institut EMI

## Slide 53: Materials for Fusion Energy Systems
Extreme operating conditions on materials surrounding the plasma:
high heat fluxes
sputtering/redeposition
T2 retention
Key strategies for the coming decade:
exploratory testing in prototypic fusion radiation environments (combined with modeling) to foster the development of candidate materials
Key issues in fusion materials degradation
Structural materials: dimensional stability and mechanical properties
Diagnostic materials: strong changes in electrical and optical properties
Key strategies for the coming decade :
new high density structural materials with nanoscale features conferring improved mechanical strength and radiation resistance

## Slide 54
Laser irradiation studies for fusion reactor materials
Lungu, Ursescu et al, APL2014
SEM W probe SEM C probe SEM Be probe

## Slide 55: Materials for Fission Energy Systems
Very High Temperature Reactor Purpose:
More Efficient Power production
Inherent passive safety features
Breakthroughs needed
materials for extreme environments, high temperature, high radiation flux, high corrosivity

## Slide 56
Testing of new materials for accelerator components
High power targets: production targets for radioactive beams, neutrinos, spallation targets
Potential collaborations: RADIATE, PASI
Secondary collimators for HL-LHC
-innovative materials are needed for accelerator collimator jaws for the upgrade of the LHC
-aims of collimator material experiments at ELI-NP: testing of novel materials under extreme conditions (accidental beam impact), quantifying of material damage for LHC operating scenarios
Notes: 56

## Slide 57
• Due to its use on low‐Earth orbits, most consumer electronics is less tolerant to
radiation effects, as communication (commercial) satellites are exposed to far less
radiation than those placed on Geostationary orbits
• Sensors with increased ability used to gather satellite data
• Increased data traffic between satellites or back to Earth →need for more
powerful algorithms and more logic in a smaller space, as satellite costs have to be
“redimensioned “
• Power issues (solar cells), thermal issues and payload issues (processing large
amounts of data and making decisions or send data to the ground)
• Processing power has to be “adjusted” to data traffic while using as little power as
possible →shrinking of transistor size : 90 nm technology → worsening SNR
• Survival of 90 nm technology to aggressive space environment conditions
• Low voltages susceptible to radiation interference
• New technologies on the consumer market : wide‐bandgap technologies
• Radiation effects: total dose, constant bombardment of radiation and low dose
rate effects
Radiation-hard Space Electronics

## Slide 58
Dynamic Response of Structural and Functional Space Materials to Micro-Meteoroid Impacts
Space environments are very hostile to many spacecraft materials and components due to the combined action of radiation, extreme temperature, and vacuum conditions, as well as impacting hypervelocity micro-particles:
Can be investigated using shock waves induced with flyers launched in high-power laser impacts on specially designed targets. These experiments can be performed both on pristine materials and on samples that have been exposed to increasing cocktail doses of particles, simulating the natural radiation exposure in space.
19 mm crater in the High-Gain
Antenna of the Hubble Space Telescope
Thousends of impacts on solar panels

## Slide 59
The radiation environment used for ground testing should ideally be similar to the natural environment probed by the satellite
This condition is difficult to achieve by traditional accelerator facilities
Cosmic radiation includes protons, helium and heavier ions, and also electrons, neutrons, and ultraviolet radiation. In this complex radiation environment many materials are damaged and deteriorate in a complex manner
The energy spectrum of laser accelerated particles is quite similar to the natural one (exponential energy distribution), unlike the quasi mono-energetic spectrum of accelerated particle beams in classical accelerators → develop rad hard testing procedures and standards
Vacuum and extreme temperatures as well as thermal cycling alter physical properties and lead to material fatigue.
Impacts of micro-meteoroids and orbiting man-made debris can damage spacecrafts and components.
Ground testing of space materials in extreme conditions

## Slide 60
Irradiated optical components testing
-characterization of optical components placed in the vicinity of laser driven
secondary radiation sources
-measuring the damage threshold modification at ISOTEST (INFLPR)

## Slide 61
E5 experimental area (2x1PW@1Hz)

## Slide 62: Layout E5

## Slide 63
TDRs to be completed between
Fall 2014 and Winter 2015
General workshop: Oct-Nov 2014
TDRs evaluated by independent reviewers March-May 2015
International Scientific Advisory Committee final endorsement of experiments in June 2015
Following steps

## Slide 64
ELI-NP Team, March 5, 2013
Thank you!
Your collaboration is decisive and a must for ELI-NP